The power to achieve

the power to achieve

A Professional Development Program

for the Mountbatten Brailler

Workshop One

Mountbatten Easy Guide

© October 2010

Harpo Sp. z o. o.

Poznan

Poland

www.mountbattenbrailler.com

Contents

Introduction	3

Mountbatten Orientation - Parts	4

Location of Parts	5

Mountbatten Orientation - Ports	6

Location of Ports	6

Features for loading paper	7

Loading Paper	9

Start-Up	10

Ways to adjust noise level	10

Battery Care	11

The Mountbatten Keyboard	12

Using the Mountbatten Keyboard	13

Turning Commands On and Off	14

Why do we use commands?	15

Speech Commands	16

Formatting Commands	16

File Commands	17

Connecting Mountbatten to a PC with MB-Comm	19

Chat Mode using the PC with MB-Comm	21

Embossing from the PC with MB-Comm	22

Embossing Commands	24

Using the Mimic	25

Saving Mimic data on the PC using MB-Comm	26

Forward Translation Commands	27

Changing the Braille Code	28

Forward Translation Commands on the MB and Keyboard	Błąd! Nie zdefiniowano zakładki.

Back Translation	29

Writing Numbers in a Command	29

Braille Writing Commands	32

Miscellaneous Commands	33

BANA characters and contractions	34

Student Evaluation Tool	35

| Introduction |
| --- |
| This guide has been prepared to provide you with a quick reference tool to use: during Workshop One as a resource when using your Mountbatten During the Workshop, we suggest you mark the Easy Guide to help you remember those sections covered. Some information in the Easy Guide is introduced, but not applied. This allows those already familiar with the Mountbatten to access information when needed, and for those beginners who want to go ahead! |
| Suggestions: | Store the Easy Guide near the Mountbatten. Introduce the Guide and how to use it to all those who may need to access the information, such as the Aide, Class Teacher and the student. Copy any procedures used regularly and put them on the wall near the Mountbatten for easy reference. Braille out reference information as the student user learns about the Mountbatten parts, ports and functionality so that they build skills of independence! |

| Mountbatten Orientation - Parts |
| --- |
| Keyboard | Ergonomically designed, yellow keyboard with six black Braille keys and seven blue keys that tell the Mountbatten what to do. |
| Embossing head | Silver metal with yellow marker to help indicate position on the page. On start-up, the embossing head moves to the right hand margin and back to identify paper size. |
| Reading Table | A flat silver metal section on which to press when reading. The table has a groove along it to align the top of the page. Lay a new page flat on the table to assist with loading paper. |
| Margin Adjusters | Both margin adjusters have grip wheels to help feed the paper through. The left margin adjuster is fixed. The right margin adjuster moves to accommodate paper size. |
| Paper Bail | A long metal bar with two rubber wheels that sit across the reading table. The paper bail holds paper in place during embossing. is spring loaded for easy removal. Slide the right hand margin to far right, grip paper bail and push to left to remove. It is best removed when a child is writing and reading Braille, giving unimpeded access. |
| Paper Lever | A yellow plastic lever, located to the right of the embossing area, lifts up and back. When lifted it releases the right margin adjuster and prompts an audio response. When returned to lock position, the audio response prompt says “OK” and the embossing head checks for the size of the page inserted by moving between the margin adjusters. |
| Ruler | A scale bar at the front of the embossing area to help re-align a Brailled page. |
| Paper Advance | A yellow plastic grooved roller located to the left of the reading table. Assists with moving a new page into position. |
| On/Off Switch | Located on the left front is the on/off switch. |
| Volume Control | At the front of the Mountbatten and to the right of the on/off switch is a thin yellow knob for volume control. |
| Carry Handle | In the center front is the yellow carry handle. Pull it out and use it to carry the Mountbatten about |

# Location of Parts

Left Margin Adjuster

Right Margin Adjuster

[movable]

Embossing Head

Keyboard

Ruler

Paper Advance

On/Off Switch

Volume Control

Carry Handle

Reading Table

Paper Lever

| Mountbatten Orientation - Ports |
| --- |
| Starting from the right-hand side of the Mountbatten: |
| USB Port | The USB port on the right side of the case is for making a connection with a PC for Chat, File transfer or embossing. |
| Mimic Port | The Mimic port on the right side of the case is for connecting the optional Mimic display. |
| PC Keyboard Port | On the back right rear of the unit is a round PS2 port for a standard PC keyboard plug. |
| Parallel-Out Port | Next is a Parallel Out port for sending information to a standard text printer directly from the MB. |
| Serial Port | The Serial port provides two-way file transfer options to and from a PC or Braille note taker, and MB-Comm software facilitates a simple file transfer program between the Mountbatten and PC. |
| Speaker | On the left side of the Mountbatten is the speaker for audio output. |
| Headphone Port | A small socket for a standard headphone jack is located next to the speaker. |
| AC Adapter Port | An AC Adapter input for mains power supply - this is for the mains charger supplied with every Mountbatten. |
| DC Adapter Port | A small socket near the corner supports an optional 12 Volt battery charger. |
| Keyboard Port | Beside the On/Off switch is a port suitable for customised external keyboards to meet special needs. |

# Location of Ports

Right side profile

Left side profile

Back profile of Mountbatten

PC Keyboard Port : PS2

Parallel Port

Serial Port

# Features for loading paper

Paper bail

Reading table

Margin adjuster

Paper  advance wheel			Embossing head			Paper lever

| Embossing head | moves along behind the ruler and embosses Braille dots. The pointer on the embossing head leads your finger to the ruler. |
| --- | --- |
| Paper lever | is on the right - raise it to insert or remove paper. |
| Reading table | is the flat strip of metal which supports paper. |
| Metal groove | in the reading table assists to align the top of the page to make sure it is straight |
| Paper bail | is the round bar that goes from left to the right above the reading table. When Brailling whole pages the rollers assist with noise reduction. It is spring loaded for easy removal. |
| Margin adjusters | the left margin is fixed, the right margin adjuster can be adjusted to paper size. Rollers on the margin adjusters grip paper while brailling. |
| Manual paper advance | is a knob set in a recess to the left of the paper control area. Use it to adjust the top edge of paper when you are inserting a new page. |
| Attention!! | Do not use manual paper advance at other times - you will lose the ability to correct or erase. |

| Loading Paper |
| --- |
| Step One | Lift the yellow paper lever. |
| Step Two | Slide the right margin left or right to make room if necessary. |
| Step Three | Lay the page flat on the reading table. |
| Step Four | Guide the paper under the embossing head. |
| Step Five | Push the paper carefully into the Mountbatten. |
| Step Six | Check that the paper is placed straight against the left hand margin and under the left grip wheel. |
| Step Seven | Align the top of the sheet of paper with the groove at the front edge of the reading table. |
| Step Eight | Hold the right side of the paper against the paper roller with your left thumb, and hold the edge up with your left index finger. |
| Step Nine | With your right hand, slide the right margin to the left, until it rests against the right edge of the paper. The paper should slide easily under the right grip wheel and over the base of the margin adjuster. |
| Step Ten | Flip the yellow paper lever back down. The embossing head will move to check the paper size. |

| Start-Up |
| --- |
| Step One: Plug in | Use the information on Ports on Page 3. Plug in the AC power adapter and switch on the power. If it is not possible to have a power connection during usage, make sure the battery is re-charged after 8 hours of use. |
| Step Two: Switch on | The On/Off switch is on the left front of the Brailler. Each time you turn the machine on the embossing head moves to check the paper size |
| Step Three: Listen | The audio response will greet you and tell you if: the battery is charging you are using Learn or Advanced Mode if the Mimic is not connected |
| Note: | If the Mimic is connected audio response will not tell you |
| Ways to adjust noise level |
| Embossing sound | The sound of the Mountbatten writing Braille can be minimised in a number of ways: place the Mountbatten on a soft surface like 2 computer mouse pads use regular photocopy paper and turn impact force or Braille pressure to a minimum place the Mountbatten in front of a solid object such as a book or facing wall |
| Speech sound | At times where a quieter class environment is needed: adjust the volume use headphones |

| Battery Care |
| --- |
| The Mountbatten needs power! It uses a lot of power when embossing and has a specially designed battery. The battery will operate the Mountbatten for up to 8-hours [or a day in class]. After this it MUST BE RECHARGED! If possible connect the power adapter provided, at all times. Otherwise, use the power adapter overnight to recharge the batteries. It is important to remember the following battery care tips: Each time you switch the Mountbatten on, it will tell you the battery status. It will tell you to charge the battery if it is low. It is a good idea to charge the battery overnight. If the battery is not re-charged when completely run down, permanent damage may result. Replacing a battery is expensive and often inconvenient. It is a good idea to leave the Mountbatten plugged in wherever possible to ensure the battery is kept charged. You need to charge your battery for at least 24 hours prior to storing it over period of up to 6 weeks. To maintain battery when Mountbatten is disconnected for longer periods, call your supplier and disconnect battery. You can check battery status by entering: ‘New line’ ‘Space’ and ‘B’ and an audio response will tell you the status. |
| The Mountbatten Keyboard |
| Braille Keys |
|       The Braille Cell | The Swing Cell |

# Using the Mountbatten Keyboard

## Moving around the page

tab	Moves the head one tab stop to the right

backtab	Moves the head one tab stop to the left

backspace	Moves the head one space to the left

newline	Moves the head to the left and advances the paper one line

space	Moves the head one space to the right

## Erase and Correct

space + backspace

backspace + the correct dots	Erase  - replaces a character with a space

Correct - replaces a character with desired character

## More moving around the page

newline + backspace	Move one line up the page in the same column

newline + space	Move one line down the page in the same column

newline + enter	Eject the paper

## Brailling on small sized paper

newline + space	Allows Braille writing without paper.

The two keys must be pressed while the embossing head is moving.

| Turning Commands On and Off |
| --- |
| Learn Mode | In Learn Mode, the command key is disabled in the default setting. |
| To activate commands | Press the following 4 keys together: space + newline + tab + backtab To deactivate press the same 4 keys together. This is called an on/off toggle. |
| Entering commands | Press the command key Type the command using Braille keys Press the enter key |
| Writing commands | Commands combine function keys and Braille letters. For example: entering a command on the Mountbatten, use the Command Key, Braille code, Enter Key; on the PC use the Escape, text and the Enter key. |

# Why do we use commands?

| In Learn Mode | Commands are used in Learn Mode to tell the Mountbatten to: set margins, tabs, line spacing and centring adjust dot height and paper settings turn embossing on and off give Braille page formatting commands eg page numbers, word wrap save files to memory and emboss and delete files use graphics mode |
| --- | --- |
| In Advanced Mode | Commands are used in Advanced Mode to tell the Mountbatten to: continue to perform all Learn Mode functions do forward and back translation provide structured introduction of Grade 2 Braille contractions [using APH patterns] do advanced editing of files in memory control synthetic speech parameters |
| Toggle keys | Command keys are usually ‘toggle’ keys. This means you repeat the command to undo it. |
| HINTS | Never use a space at the beginning or end of a command If you make a mistake while entering a command, press the ‘command’ key to start again. |

| Speech Commands |
| --- |
| For use with recorded and synthetic speech. |
| spk r | Speaks recorded speech (default) In MB Writer this command indicates the speaking mode is selected |
| spk a | Speaks all keyboard keys, functions and commands |
| spk d | Speaks dot keys only – no function keys |
| spk c | Speaks commands, errors and prompts only – no dot keys |
| spk n | No speech – tones only |
| spk s | Speaks synthetic speech (only available in MB Pro) |

| Formatting Commands |
| --- |
| ww | Word wrap |
| ce | Center text (default off - toggle) |
| ra | Right adjust (default off - toggle) |
| Margins |
| lm | Set left hand margin to 0 |
| lmh | Set left hand margin to embossing head position |
| lm[n] | Set left hand margin [n = number of columns] |
| rm | Set right hand margin to 0 |
| rmh | Set right hand margin to embossing head position |
| rm[n] | Set right hand margin [n = number of columns] |
| tm[n] | Set Braille top margin [n = number of lines] |
| bm[n] | Set Braille bottom margin [n = number of lines] |
| Tab Settings |
| tsh | Set tab at position of embossing head |
| tc | Clear all tab settings |
| Line Spacing |
| ls 1 | Line spacing 1 |
| ls 1.5 | Line spacing 1.5 |
| ls 2 | Line spacing 2 |

| File Commands |
| --- |
| Start a File |
| begin [filename] | Opens a new file – filenames can have up to 16 characters |
| Close a File |
| end | Closes an open file |
| Finding out what’s in the memory |
| dir | Embosses all file names and their sizes |
| free | Embosses all remaining free memory space |
| Change a File |
| Append [filename] | Attaches more information to a file |
| rename filename1, filename2 | Renames ‘filename1’ and calls it ‘filename2’ |
| Delete Files |
| del [filename] | Deletes a file |
| del all | Deletes all files |
| undel | Retrieves the last deleted file. This command only works if used before turning the unit off. |
| Emboss Files from the Memory |
| pr [filename] | Prints the file |
| mpr n [filename] | Prints ‘n’ copies of file |

| Connecting Mountbatten to a PC with MB-Comm |
| --- |
| Switch Mountbatten OFF | Always switch off before making a connection to the MB. |
| Step by step: | Load the Mountbatten with paper |
|  | Identify the USB port on the MB and the PC |
|  | Connect the MB and the PC using the cable. |
|  | Find the MB-Comm Icon and run MB-Comm. |
|  | Run MB-Comm and make the connection. |
|  | You can make the connection in one of two ways: |
| Click the right-hand red button |  |
| OR |  |
| On the Device Menu, click Connect Mountbatten |  |
| Choosing the Port | A dialog box will appear on the screen: |
| Important! | Make sure you choose the correct port before you continue. |
| If you are using USB | The port you choose MUST say "Mountbatten USB". |
|  | Click OK when you have chosen the port. |
| Making sure everything is ready... | Next you will see a reminder: |
| ...and then completing the connection. | If you are happy that everything is ready, click Continue. |
| What will happen? | The Mountbatten will make a series of short, high-pitched beeps. The red buttons will turn green one at a time. When the connection is complete, both buttons will be green. |
| You are now ready to use MB-Comm. |

| Chat Mode using the PC with MB-Comm |
| --- |
| Producing translated Braille and Print simultaneously in real time |
| Important! | Mountbatten must be on and loaded with paper The PC and Mountbatten must be connected MB-Comm must be running and connected The two buttons on the MB-Comm screen must be green |
| Enter Chat Mode | Go to the File Menu in MB-Comm and click "Chat Mode" Mountbatten will say: "Back" This means that the Braille keyboard will send translated text to the MB screen. |
| Change between users | To change to the PC keyboard, the Braille user must press the tab key on the Mountbatten. Mountbatten says "Forward" To change to the Braille keyboard, the Braille user must press the backtab key on the Mountbatten. Mountbatten says "Back". |
| Important! | The Braille user on the Mountbatten keyboard types first - the Braille keyboard Back Translation is ready first changes between Forward and Back Translation using tab and backtab |
| The PC keyboard user | Types text produces Grade 2 Braille on the Mountbatten produces text on the MB-Comm screen |
| The Mountbatten keyboard user | Types Braille produces Braille on the Mountbatten produces text on the MB-Comm screen |
| Embossing from the PC with MB-Comm |
| Producing a translated Braille copy from a text file on the PC |
| Preparing the file | Save the file as Plain Text with a .txt extension Open the file in Notepad Insert any commands you need at the beginning of the file {adv} if the Mountbatten is in Learn Mode {fe} to have Mountbatten translate the file {flit} to preserve print lines in Braille {fgr 1} to have Uncontracted (Grade 1) Braille {m} to emboss at double speed Insert any commands you need at the end of the file {adv} to return to Learn Mode {m} to return to normal speed Save the file again |
| Important! | Insert your commands on a new line by themselves! |
| Tip: | Have a folder on the PC to store ready for your text files to be embossed. Always save to this folder so you can find them again. |
| Run MB-Comm and connect to the PC | See the instructions in previous sections Make sure you prepare the Mountbatten before you begin! |
| From the File Menu select Emboss file to Mountbatten | MB-Comm will ask you to choose the file. Navigate to the file and select it. Click OK. Mountbatten will begin embossing the translated file. |
| Tip | Save a Notepad file with only the commands in it to use as a template. Copy and paste directly from a Word or OpenOffice document into your template. |

| Embossing Commands |
| --- |
| Using Continuous Paper |
| cp | Continuous paper feed (default off - toggle). |
| cpa n | Adds or subtracts ‘n’ to form length of continuous paper. |
| Paper Size |
| fl n[.m] | Sets physical length of page in inches or centimetres. |
| Page Numbering |
| pn [n] | Begins page numbering, starting at ‘n’. |
| Controlling the Braille Output |
| el [n] | Allows only ‘n’ empty lines while embossing to avoid large blank spaces when embossing. |
| cap | Caps lock (default on - toggle). |
| Using the Mimic |
| Text display on LCD screen | Print words appear accurately, irrespective of student brailing contracted or uncontracted Braille Text appears after the space bar is pressed |
| Learn Mode | The Mimic works automatically in Learn Mode. If unplugged or switched off the MB Pro will say “Mimic off”. It does not however, say “Mimic on”. |
| Advanced Mode | The Mimic needs to be activated in Advanced Mode. |
| On/Off switch | The switch is located at the rear left of the unit and needs to be switched on after being connected to the Mountbatten. The Mimic runs on 4 AA batteries or a 6 Volt adaptor. |
| Automatic shut-down | If not used for 15 minutes the Mimic will shut down. To re-activate, touch any key. |
| Mimic Keypad | Press keys firmly for more than 1 second to activate. Under the display screen there are three buttons. |
| Scroll Up | Press left button – one short beep. Scrolls up 20 characters of text. |
| Scroll Down | Press right button – one short beep. Scrolls down 20 characters of text. |
| Set Bookmark | Press left and center button – two long beeps. |
| Clear Memory | Press left and right buttons together for 2 seconds. Will erase the text on the screen. |

| Saving Mimic data on the PC using MB-Comm |
| --- |
| Prepare the Mimic | If you only want part of the Mimic's contents, set a bookmark at the beginning of the text you want to send. To set a bookmark, press and hold the left pushbutton and the center pushbutton together (see the picture on the Mimic). When the two pushbuttons are pressed together, they must be held down for one second before the bookmark will be set. You will then hear two beeps and a B will appear on the right side of the screen indicating the position of the bookmark. Mimic will send everything from this bookmark to the next bookmark, or to the end of the memory if there is no other bookmark after this. |
| Check the Mimic User Guide | See also the pushbutton picture guide on the face of the Mimic. |
| Connect Mimic to the PC serial port | This connection uses the Serial Port on the back of the Mountbatten. Check the Ports in the Easy Guide to identify the right port. Make sure you read about Port Speed in the steps below. This connection uses the Mimic Serial Cable. If your computer has no Serial Port, you might need a USB-to-Serial converter - check with your distributor to obtain one. When you are using a USB-to-Serial converter, you need to know which COM port it uses. |
| Turn off the Mimic | Connect the cable to the Mimic and PC while the Mimic is off. |
|  | Turn the Mimic on. |
| Run MB-Comm | Instead of clicking Connect Mountbatten, click Connect Mimic |
|  | When the Select Port dialog comes up: |
|  | Select the correct COM port (not Mountbatten USB!) Ask your distributor or IT personnel for assistance if you need it to find this out |
|  | Click the Settings button |
|  | Change the Port Speed from 115200 to 9600 |
|  | Click OK |
|  | Click Continue |
|  | On the MB-Comm File menu, choose Receive and Save file from Mimic MB-Comm is now waiting for the Mimic to send. |
| Starting the transfer from the correct place | Jump to the bookmark at the beginning of the text you want to send: Press and hold the center pushbutton for half a second. Don't scroll to the bookmark, as your transfer won't begin from the right place. |
| Sending the Data | Press all 3 Mimic pushbuttons down and hold for 2 seconds. The screen will display Sending Memory... When the transfer is complete you will hear 3 beeps. |
|  | If you have no bookmarks set, all the data in memory will be sent. |

| Forward Translation Commands |
| --- |
| Switch to Advanced Mode (command)adv(enter) |
| Turn on Forward Translation |
| fe fe [filename] | Forward translate and emboss Forward translate and emboss file |
| fm | Forward translate and send to memory |
| fm end | End file and turn embossing back on |
| Change Braille Grade or Code |
| fgr [grade] | Change grade (fgr 1 for Grade 1; default Grade 2) |
| ffc [language] | Foreign character selection - refer to the table on the next page |
| Formatting Your Braille |
| flit | Literal mode – a new print line begins a new Braille line |
| flit [n] | Creates a hanging indent (n=0 - 5) |
| flit s | Suppresses blank lines and adds a 2 cell indent to new paragraphs |
| fit | Italics |
| fin | Stores current Braille column for indent |
| fsh | Multiple space removal |
| Lists/ Tables |
| flist | Creates 2 column table |
| flist n1n2 | Creates 3 column table |
| Saving Preferred Format Settings |
| save ft | Saves Forward Translation settings |
| std ft | Restores all default Forward Translation settings |

| Changing the Braille Code |
| --- |
| ffc [language] | Forward translation followed by country code |
| bfc [language] | Back translation followed by country code |
| Country Codes | OZ = Australian ITL = Italian DAN = Danish NOR = Norwegian UK = English SP = Spanish FR = French SWE = Swedish GER = German USA = United States GRK = Greek DUT = Dutch FIN = Finnish POR = Portuguese |

| Back Translation |
| --- |
| bp | Commence back translation to printer. Automatically print a text copy and emboss at the same time |
| em | Turn embossing off (default on – toggle) |

| Writing Numbers in a Command |
| --- |
| Option 1 | Use number sign, then number |
| Option 2 | Use dropped Nemeth number |

# The Options Menu

| The Options Menu provides access to many of the new and exciting features of the MB LS. To use the Options Menu you must be in Advanced Mode. Refer to the User Manual for detailed operation of each Option. |
| --- |
| o-chord | The Options menu is accessed by pressing the letter O and the Space key together. O-chord is followed by a letter to access the options listed below. |
| z-chord | To exit any of the Options use the z-chord (z plus Space). |
| Music |
| o-chord u | Simple Music mode. Intended for fun and pre-braille |
| o-chord u-chord | Music Mode. Enter a Braille music character and hear it played back |
| Stopwatch |
| o-chord w | Turns on a stopwatch. Test skills, time activities. Have fun. |
| Time and Date |
| o-chord d | Speak Date |
| o-chord t | Speak Time |
| o-chord s | Set Time and Date |
| Mathematics |
| o-chord m | Turn on a simple Maths calculator. |
| o-chord n | Nemeth mode. In literary Braille, Nemeth characters will be spoken as numbers |
| o-chord c | Turn on a full scientific calculator |

| The Options Menu - Music |
| --- |
| Music – Simple Mode and Play Mode |
| o-chord u | Simple Music mode. Intended for fun and pre-braille. |
|  | The six dot keys and the command key become a scale. Press each key sequentially: 3 2 1 Command 4 5 6 Press the same keys again to hear the scale in a higher octave. |
|  | Other keys have the following functions: backspace Move scale down an octave enter Move scale up an octave space Extend the note by a quarter bar/crotchet newline Extend the note by a half bar/minim newline + space Extend the note by a full bar/semibreve tab Flat backtab Sharp Press multiple note keys together to hear a chord (maximum number: three notes). |
| o-chord u-chord | Music Play Mode. Enter a Braille music character and hear it played back |
|  | In the play mode, students can type Braille music characters and hear them being played at the same time. This mode is intended for students who are just starting out learning Braille and becoming familiar with the Braille music code |

# Braille Music - the notes

| C | D | E | F | G | A | B | Rests | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Y y | Z z | & & | = = | ( ( | ! ! | ) ) | M m | Wholes or 16ths |
| N n | O o | P p | Q q | R r | S s | T t | U U | Halves or 32nds |
| ? ? | : : | $ $ | ] ] | \ \ | [ [ | W w | V v | Quarters or 64ths |
| D d | E e | F f | G g | H h | I i | J j | X 0x | 8ths or 128ths |

| Braille Writing Commands |
| --- |
| The following commands apply in both Learn Mode and Advanced Mode |
| cor | Correction Mode (When off, correcting and erasing are disabled) |
| em | Turn embossing off (default on - toggle) |
| man | Choose between manual and automatic new line (default auto - toggle) |
| ms [n] | Multi strike feature [n=1-4] can be used to Braille heavy materials |
| np | New Page or page eject |
| pn [n] | Begin page numbering |
| pbell [n] | Set page bottom warning bell to ring [n] lines before bottom of page |
| rmbell | Right Margin Bell (rings 5 positions before end of line) (default on – toggle) |
| show | Emboss commands as they are entered (default off – toggle) |

| Miscellaneous Commands |
| --- |
| newline + space + b | Checks battery status |
| ku | One Handed Mode (default off - toggle) |
| ver | Embosses Brailler software version |
| hp | Help. Embosses command summary |
| save | Saves all current settings |
| std | Restores back to factory settings |
| alt n | Enters non-standard ASCII characters |
| Making Braille Graphics |
| gf | Reduces space between dots so that lines can be drawn (default off – toggle) |
| Adjusting Dot Height |
| backtab + command | Increases impact |
| tab + command | Decreases impact |
| ms [n] | Multi-strike (n=1 to 4) |
| Opening the Serial Port |
| S1 | Opens the Serial Port so that text can be read on the Mimic while a PC keyboard is in use [forward translation] |

# BANA characters and contractions

| a | b | c | d | e | f | g | h | i | j |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| a | b | c | d | e | f | g | h | i | j |
| k | l | m | n | o | p | q | r | s | t |
| k | l | m | n | o | p | q | r | s | t |
| u | v | x | y | z | & | = | ( | ! | ) |
| u | v | x | y | z | and | for | of | the | with |
| * | < | % | ? | : | $ | ] | \ | [ | w |
| ch | gh | sh | th | wh | ed | er | ou | ow | w |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 |
| /ea/, | be/ bb/ ; | con/ cc / : | dis/ dd / . | en | to/ ff/ ! | were (/gg/) | his "//? | in | was by/ / |
| / | + | # | > | ' | - |  |  |  |  |
| st | ing | num/ ble/ ble | ar | ' | com - |  |  |  |  |
| @ | ^ | _ | " | . | ; | , |  |  |  |
| dot 4 | dot 4,5 | dot 4,5,6 | dot 5 | dot 4,6 | letter sign | cap |  |  |  |

© 2010 Harpo Sp. z o. o.

ul. 27 Grudnia 7

61-737 Poznań

Poland

t: +48 61 853 1425

f: +48 61 853 1419

info@harpo.com.pl

HARPO

# Student Evaluation Tool

## For Teachers and Para-professionals

This evaluation tool gives educators a basic skills checklist that can help in evaluating skills developed as the student learns to use the Mountbatten for every-day activities.

The list can be used to set achievable objectives when drawing up instruction plans.  Dating when skills were acquired will assist in measuring growth and provide a basis for review.

Space has been left at the bottom of each section for comments to assist with monitoring.

| Student Name: | Class: |
| --- | --- |
| School: |
| Assessing Teacher: | Date: |

## 1. Mountbatten Orientation – Parts:

| OBJECTIVE | YES | DATE |
| --- | --- | --- |
| Student can turn Mountbatten on and off |  |  |
| Student knows location of all 6 Braille keys |  |  |
| Student knows the dot number for each key |  |  |
| Student can operate volume control |  |  |
| Student can locate the following parts of the Mountbatten: |  |  |
| Paper lever |  |  |
| Margin adjusters [left and right] |  |  |
| Embossing head |  |  |
| Paper advance knob |  |  |
| Student knows the location of the blue keys: Space bar |  |  |
| Back space |  |  |
| Newline |  |  |
| Enter key |  |  |
| Command |  |  |
| Tab |  |  |
| Backtab |  |  |
| Student knows how to care for equipment: No food or drink near equipment |  |  |
| Clean hands before use |  |  |
| Turn off after use |  |  |
| Use of power supply |  |  |
| Care of battery |  |  |
| Keep away from desk edge |  |  |
| Location of carry handle |  |  |
| Portability care |  |  |

### Comments:

## 2. Mountbatten Orientation – Ports

| OBJECTIVE | YES | DATE |
| --- | --- | --- |
| Student can locate the following ports and identify the appropriate plug: Headphone port and jack |  |  |
| Power adapter port and plug |  |  |
| PC keyboard port and plug |  |  |
| Serial and Parallel printer ports |  |  |
| Serial cable and plug |  |  |
| Parallel cable plug |  |  |
| Mimic port |  |  |
| Mimic cable and plugs |  |  |
| Student will understand the concepts: Left front |  |  |
| Right front |  |  |
| Left back |  |  |
| Right back |  |  |
| Left side |  |  |
| Right side |  |  |

### Comments:

## 3. Set-up:

Note:  Being able to successfully plug in all connecting devices is a fine motor skill which requires development through assistance and instruction.  This set of Objectives along with Objective 8, 9 and 10 may best be assessed when the skills required are developed rather than when they are first introduced.

| OBJECTIVE | YES | DATE |
| --- | --- | --- |
| Student can connect the power adaptor to the Mountbatten and switch it on |  |  |
| Student can switch Mountbatten on and off |  |  |
| Student is aware of content of recorded speech output on Mountbatten at start-up (with and without Mimic connected) |  |  |
| Student is aware of recorded speech response when Brailling |  |  |
| Student can connect the headphones and use the volume control |  |  |

### Comments:

## 4. Loading Paper

| OBJECTIVE | YES | DATE |
| --- | --- | --- |
| Student can remove and replace paper bail |  |  |
| Student is aware of audio response when paper leaver is lifted |  |  |
| Student can load photocopy paper from the top |  |  |
| Student can load Braille paper from the top |  |  |
| Student can align paper with groove on reading table and position it correctly under wheel of margin adjusters |  |  |
| Student can decrease Braille pressure |  |  |
| Student can increase Braille pressure |  |  |
| Student can remove paper manually |  |  |
| Student can use automatic page eject |  |  |
| Student can correctly load a pre-brailled worksheet |  |  |

### Comments:

## 5. Brailling in Grade 1

| OBJECTIVE | YES | DATE |
| --- | --- | --- |
| Student can place fingers on Braille keys correctly |  |  |
| Student can use space key and new line key |  |  |
| Student can type Grade 1 Braille |  |  |
| Student can use audio response to support action |  |  |
| Student can identify and understand when to use Command key |  |  |
| Student can use reading table to track progress |  |  |

### Comments:

## 6. Moving around the page:

| OBJECTIVE | YES | DATE |
| --- | --- | --- |
| Student can erase |  |  |
| Student can erase and correct |  |  |
| Student can move down page without moving embossing head |  |  |
| Student can move up the page without moving embossing head |  |  |
| Student can move across the page and back to left margin |  |  |
| Student understands the use of and can switch on Word Wrap |  |  |
| Student can centre a word |  |  |
| Student can set double line spacing |  |  |
| Student can widen left margin |  |  |
| Student can insert page numbers |  |  |
| Student can execute a command sequence accurately |  |  |

### Comments:

## 7. Creating and Saving Files in Memory

| OBJECTIVE | YES | DATE |
| --- | --- | --- |
| Student can start and name a file |  |  |
| Student can end a file |  |  |
| Student can emboss a directory |  |  |
| Student can select a file name |  |  |
| Student can emboss the contents of a stored file |  |  |

### Comments:

## 8. Connecting Devices – Mimic

Note:  Being able to successfully plug in all connecting devices is a fine motor skill which requires development through assistance and instruction.  This set of Objectives may best be assessed when the skills required are developed rather than when they are first introduced.

| OBJECTIVE | YES | DATE |
| --- | --- | --- |
| Student can identify Mimic port and connect the Mimic |  |  |
| Student can switch on Mimic |  |  |
| Student is aware of changes to audio output on start-up |  |  |
| Student knows to press space to send information to Mimic |  |  |
| Student knows that in Learn Mode text is displayed automatically |  |  |
| Student is aware of the automatic shut-off feature |  |  |
| Student is aware of and can activate the wake-up feature |  |  |
| Student is familiar with the functionality of the Mimic |  |  |

### Comments:

## 9. Connecting Devices – PC keyboard

Note:  (1) Being able to successfully plug in all connecting devices is a fine motor skill which requires development through assistance and instruction.  This set of Objectives may best be assessed when the skills required are developed rather than when they are first introduced.

(2) Learning the layout of the QWERTY keyboard is a separate skill development exercise.

| OBJECTIVE | YES | DATE |
| --- | --- | --- |
| Student is aware of the correct procedure when connecting a PC keyboard [switch off Mountbatten prior to connecting PC keyboard] |  |  |
| Student can identify the correct port and plug in the PC keyboard |  |  |
| Student is aware of the main features of Advanced Mode |  |  |
| Student can activate Advanced Mode and return to Learn Mode |  |  |
| Student understands the concept of Forward Translation |  |  |
| Student knows the command for Forward Translation |  |  |
| Student can listen effectively to synthetic speech |  |  |
| Student is aware that Grade 2 Braille is the automatic default in Advanced Mode |  |  |
| Student is aware of the advantages of the PC keyboard for sighted users |  |  |

### Comments:

## 10. Connecting Devices – Printer

Note:  Being able to successfully plug in all connecting devices is a fine motor skill which requires development through assistance and instruction.  This set of Objectives may best be assessed when the skills required are developed rather than when they are first introduced.

| OBJECTIVE | YES | DATE |
| --- | --- | --- |
| Student is aware of correct procedure when connecting a printer [Switch off Mountbatten prior to connecting printer] |  |  |
| Student can identify the correct port and can plug in the printer |  |  |
| Student can identify plugs and insert them correctly |  |  |
| Student can check for paper in printer |  |  |
| Student understands the concept of Back Translation |  |  |
| Student can turn on Back Translation |  |  |
| Student can send a file to be embossed & printed simultaneously |  |  |
| Student can send a file to be printed only |  |  |
| Student understands the buffer behaviour and can activate it |  |  |
| Student can use correct procedure to disconnect the printer |  |  |

### Comments:

## Final comments:

Use this space to write any other comments especially when a student is to move to a new teacher.

# Text boxes

Headphone socket

Mimic port

AC adapter port

USB port

DC adapter port

Speaker